## Slide 1
(a) Entropy-coded transmission and recovery
Transmitter (Tx)
Receiver (Rx)
Image x
(256 × 256 × 3)
Frozen VAR tokenizer
Visual encoder
E(·)
Multi-scale
residual VQ
(shared codebook)
Frozen
Multi-scale tokens
{r₁, …, r₁₀}
⋮
⋮
s₁₀ = 16
Frame
assembly
AWGN
channel
(known SNR)
y = s + n
Decoded
token
prefix
VAR
completion
(frozen)
Codebook
lookup
rescale +
residual sum
Image
decoder
D
c
(·)
(frozen)
Reconstruction
x̂
(256 × 256 × 3)
Decoded scales 1–7
155 token indices
s₁
1 × 1
⋯
s₂
2 × 2
⋯
s₇
8 × 8
Frozen policy lookup
Input: (N, SNR)
Target (m*, K*); MCS (M, r)
Calibrated offline; queried per image
Target endpoint /
fallback chain
Frozen MCS
(M, r)
Same frozen VAR prior at Tx and Rx
CDFs reconstructed locally from token history
Data
Control
Prefix selection
All scales 1, …, m
+ first K in scale m + 1
(raster order)
Actual-length check
Lterm + 13 + 16 ≤ kLDPC
Else: step down the
frozen fallback chain
Actual endpoint (m, K)
Digital transmitter
Image payload (single LDPC codeword)
VAR-conditioned
arithmetic encoder
MCS: (M, r)
Length
13 bits
Terminated
AC stream
Zero
padding
CRC16
LDPC
QAM
Protected public header · 68 symbols
Actual profile ID
(m, K, M, r, …)
CRC
Conv. coding
+ QPSK
Digital receiver
Header decode
→ actual profile
QAM demap
→ LDPC decode
CRC / length check
Arithmetic source
decoding
Header / CRC / length / AC failure
→ fixed gray output
Thumbnails are schematic
Entropy source-bit utilization · 10 dB · 500-source means
AC budget: 2520 = 2549 − 13 − 16 bits
WHOLE (whole scales)
77.70% AC source bits
22.30% padding
PARTIAL (within-scale)
95.21% AC source bits
4.79% padding
Same physical frame for both
68
956 coded-body symbols
68 + 956 = 1024 channel symbols
(b) Boundary-scale recovery: entropy-coded example, 10 dB, m = 7, K = 75
VAR predicts all
scale-8 tokens
10 × 10 = 100
argmax
75 decoded
scale-8 tokens
Overwrite first 75
positions (raster order)
Scale 8 (merged)
75 decoded + 25 predicted
= 100 tokens (10 × 10)
Advance with
merged scale-8
state
Scale 9 (predicted)
13 × 13 = 169
(all predicted)
Scale 10 (predicted)
16 × 16 = 256
(all predicted)
Decoded
token
Predicted
token
Notes: System diagram revised from user-provided system_diagram_v2.pptx. Original color palette, dimensions, native token shapes and kingfisher thumbnails retained where applicable. Thumbnails are schematic, not measured reconstruction results.
Mainline: entropy-coded payload; N=1024 channel symbols, robust public header=68 symbols, coded body=956 symbols. The final actual endpoint (m,K) is signaled through the paid profile ID. Target lookup is calibrated offline; per-image terminated-length fallback holds MCS fixed.
Body before LDPC: 13-bit source-stream length, terminated arithmetic-coded stream, zero padding, CRC16. Feasibility: L_term +13+16 <= k_LDPC. Receiver rejects invalid headers, CRC/length/source parsing or arithmetic termination failures and emits fixed gray output.
Both sides use the same frozen VAR prior. Arithmetic CDFs are reconstructed locally from the token history; no CDFs or untransmitted token oracle are sent through a side channel.
Budget illustration: 10 dB, 16-QAM, LDPC k=2549 and n=3824, nominal rate2/3. Usable AC-source budget2520 bits. Across500 sources WHOLE mean AC bits=1958.134 (77.70%), PARTIAL=2399.242 (95.21%). Padding percentages complement these utilization percentages inside2520 bits. Physical-body length remains956 channel symbols for both. Percentages are aggregate means, not a single-frame bitstream.
Panel(b): an actual admissible entropy endpoint example at10 dB is m=7,K=75 (277/500 sources in the registered distribution). Coarser scales1..7 contain155 tokens. Predict full scale8 (10x10), overwrite first75 row-major positions, retain25 predicted, advance the merged state, then predict scale9 (13x13) and scale10 (16x16) sequentially. No claim that every source uses this endpoint.
Primary implementation and measurement sources at frozen repository SHA 02ee120324e3f2fa16b2b05b602346db34256586:
https://github.com/daiqizai/var-comm/blob/02ee120324e3f2fa16b2b05b602346db34256586/experiments/entropy-partial-mismatch-20261010/scripts/ep_phy.py
https://github.com/daiqizai/var-comm/blob/02ee120324e3f2fa16b2b05b602346db34256586/paper/manuscripts/nestcom_entropy_v6_20261019/manuscript.tex
https://github.com/daiqizai/var-comm/blob/02ee120324e3f2fa16b2b05b602346db34256586/results/n1024_consistency_20261019_v1/family_snr_summary.csv
https://github.com/daiqizai/var-comm/blob/02ee120324e3f2fa16b2b05b602346db34256586/results/n1024_consistency_20261019_v1/endpoint_distribution.csv
Editable master deliverable retains Times New Roman font names. PDF/PNG rendered in this environment with metrically compatible Liberation Serif because Times New Roman font binaries are absent.