## Slide 1
(a)
System overview
VAR modules share frozen weights
Transmitter
Digital link
Receiver
x
E
Image
encoder
f
Residual VQ
Rs
↓ Q
Cs
−
Rs + 1
Scale prefix
1 … m
m + 1
e = (m,K)
see (b)
Entropy
prior (VAR)
q<s
CDF
Arithmetic
encoder
LDPC
+ QAM
+
AWGN
n
Demap
+ LDPC
N complex symbols
Profile
Coded body
Arithmetic
decoder
Entropy
prior (VAR)
CDF
Recovered
profile
a
e
q̂<s
Scale completion
1 … m
m + 1
… S
Completion · see (c)
Cs
Σ
f̂
Dc
Image
decoder
x̂
(b)
Within-scale endpoints
MCS a fixed
Prefix πe
1 … m
m + 1
Arithmetic
coding
Schematic bars
η = b/(ka − 29)
Whole
Partial
Next whole
> capacity
ka
Source bits
Length + CRC
Padding
b(x,e) + 13 + 16 ≤ kₐ
(c)
Boundary-scale completion
Hm
Next-scale
prior (VAR)
argmax
Predict
Received K tokens
Overwrite
q̃m + 1
Residual accumulation
Finer-scale conditioning
Finer scales
Tokens:
Transmitted / received
Predicted
Not transmitted
Notes: Fig. 1 — NeST-Com, final editable figure.
Native shapes and text; only the two bird images are raster assets.
CAPTION
\caption{NeST-Com.
(a) The transmitter entropy-codes a next-scale token prefix with endpoint $e=(m,K)$ using CDFs from a frozen VAR. The receiver rebuilds the CDFs from decoded coarse-scale tokens $\hat q_{<s}$, and the recovered profile gives $e$ and MCS $a$.
(b) For a fixed MCS, the terminated stream of length $b(x,e)$, a 13-bit length field, and a 16-bit CRC must fit within the LDPC information length $k_a$. Within-scale endpoints raise mean source-bit utilization $\eta=b(x,e)/(k_a-29)$ from 77.70\% to 95.21\% (500 images, $N=1024$, 10 dB). The rows illustrate per-frame alternatives: WHOLE/PARTIAL segment lengths use the measured means, and next-whole overflow is schematic.
(c) At the boundary scale, the $K$ received tokens overwrite the VAR predictions, and the merged map $\tilde q_{m+1}$ conditions the finer scales. $H_m$ denotes the VAR state after scale $m$; $C_s$ comprises codebook lookup, resizing, and the scale-dependent residual transform.}
\label{fig:system}
II.B UTILIZATION
% Section II-B: replace the utilization equation and its accompanying text.
% Keep the surrounding method description unchanged.
% The percentages match Table I: WHOLE 77.70%, PARTIAL 95.21%.
For MCS $a$, let $k_a$ denote the LDPC body information length and $b(x,e)$ the actual terminated arithmetic-code length for image $x$ and endpoint $e$. Feasibility and source-bit utilization are
\begin{equation}
b(x,e)+29\leq k_a,
\qquad
\eta(x,e)=\frac{b(x,e)}{k_a-29}.
\label{eq:fit}
\end{equation}
The 29 bits comprise a 13-bit length field and a 16-bit CRC, leaving $k_a-29$ bits for the arithmetic stream. Zero padding fills the remaining $k_a-29-b(x,e)$ bits of the information block.
Reported utilization is the mean of $\eta(x,e)$ over the 500 source images. At $N=1024$ and 10 dB, $k_a=2549$ provides 2520 bits of source capacity; WHOLE and PARTIAL achieve mean utilizations of 77.70\% and 95.21\%, respectively (Table~\ref{tab:within-scale}). Fig.~\ref{fig:system}(b) illustrates alternative per-frame endpoints: WHOLE/PARTIAL source and padding segments are scaled to these measured means, while the next-whole row illustrates overflow.
Evidence: table_i.csv, N=1024, SNR=10 dB, common500. Mean source-bit utilization: Whole=0.7770373015873016; Partial=0.9520801587301587; source capacity=2520; LDPC information length=2549; overhead=13+16 bits.
Source: accepted Fig1_NeST_Com_measured_v25, with the capacity bracket explicitly labelled k_a.